## Slide 1
VR-Based Vehicle Ergonomics Testing
How We're Using Virtual Reality to Design Safer, More Comfortable Vehicles
Leadership Briefing · 2026

## Slide 2
Table of Contents
01
The Problem
Why ergonomic issues persist in traditional vehicle development
02
The Human Factor
How the human body creates design blind spots
03
Our Solution
VR-based body tracking and collision measurement
04
How It Works
Four-step workflow from setup to insight
05
What We Measure
5 body points, 3 warning levels, real-time feedback
06
Accuracy & Calibration
Per-subject body modeling and measurement specs
07
The Data
What every session produces for engineering teams
08
Business Value
Cost, speed, and decision quality
09
Current Status
Where we are and what comes next

## Slide 3
The Problem
Every car has a blind spot in the design process
10×
More expensive to fix ergonomic issues after physical prototyping
▸ Ergonomic issues are discovered too late — after manufacturing commitments are made
▸ Drivers bump their knee on the AC unit, scrape their shin on the door frame, or can't comfortably enter/exit the vehicle
▸ Physical prototypes are expensive and slow to iterate — each design change costs weeks
▸ Subjective feedback ('it felt tight') is difficult to act on — engineers need numbers
▸ A standard-size mannequin cannot capture the full range of real driver body shapes and motions

## Slide 4
The Human Factor
It's not a design problem — it's a human body problem
"The gap between 'fits on paper' and 'fits in real life' is where discomfort and injury risks hide."
Human Bodies Move in Arcs
Vehicles are measured in millimeters on a screen But a driver's knee swings in a 3D arc on entry/exit Static clearance measurements miss dynamic risk
▸ Vehicles are measured in millimeters on a screen
▸ But a driver's knee swings in a 3D arc on entry/exit
▸ Static clearance measurements miss dynamic risk
Everyone Is Different
Leg length, hip width, and entry angle vary widely A design safe for 5th-percentile female may harm 95th-percentile male One 'average' mannequin can't represent your full customer base
▸ Leg length, hip width, and entry angle vary widely
▸ A design safe for 5th-percentile female may harm 95th-percentile male
▸ One 'average' mannequin can't represent your full customer base
Motion Reveals Problems
Critical collisions happen in motion, not at rest Entry and exit sequences are the highest-risk moments These cannot be tested with a static digital model
▸ Critical collisions happen in motion, not at rest
▸ Entry and exit sequences are the highest-risk moments
▸ These cannot be tested with a static digital model

## Slide 5
Our Solution
Test the human body — before building the car
VR Virtual Reality
▸ The driver wears a VR headset and walks through a full-scale digital vehicle interior
▸ No physical prototype required
▸ Any vehicle design can be tested on the same day it is created
Body Tracking
▸ 5 sensors on the body (waist, both knees, both feet) capture exact position in real time — 90 times per second
▸ A digital body model mirrors every movement
▸ Calibrated individually to each test subject's proportions
Collision Intelligence
▸ The system automatically measures how close every body part gets to every vehicle component
▸ Three alert levels: Safe / Warning / Collision
▸ Every measurement is logged to a data file for engineering review
Real human movement. Digital vehicle. Data you can act on.

## Slide 6
How It Works
Four steps from setup to insight
1
Strap On Sensors
HMD headset + 5 Vive Trackers attached to waist, both knees, and both feet ~2 min setup
▶
2
Calibrate
Subject stands in T-Pose for 10 seconds. System measures individual body proportions. ~10 sec
▶
3
Enter the Vehicle in VR
Subject performs entry/exit sequence inside the digital vehicle. System tracks every movement. ~5 min
▶
4
Review the Data
CSV report generated: minimum clearances, warning events, collision log — ready for engineering review. ~1 min
Total time per session: ~10 minutes

## Slide 7
What We Measure
5 body points · 3 warning levels · real-time feedback
Body Tracking Points
Point
Sensor
Monitors Against
Waist / Hip
Tracker 1
Seat rail, center console
Left Knee
Tracker 2
Steering column, dashboard
Right Knee
Tracker 3
Center console, glove box
Left Foot
Tracker 4
Dead pedal, footwell floor
Right Foot
Tracker 5
Pedals, footwell
SAFE
> 10 cm clearance
No action needed
WARNING
3 – 10 cm clearance
Screen darkens · alert tone
COLLISION
< 3 cm clearance
Screen darkens fully · impact sound · visual FX at contact point
Thresholds are fully configurable per test session.

## Slide 8
Immersive Feedback in VR
The driver feels the problem — not just sees it
Visual — Screen Vignette
As a body part approaches a vehicle component, the edges of the VR display darken progressively. Full darkness at collision level — the subject's natural instinct is to adjust without verbal instruction.
Audio — Alert Tones
A soft alert tone plays at warning distance. A sharp impact sound plays at collision distance. Real-world auditory instinct takes over — no coaching needed.
Spatial — Impact Visual FX
A particle burst appears precisely where contact would occur, anchoring the collision in 3D space. Subjects look toward the contact point naturally, reinforcing body awareness.
Subjects react naturally. The data reflects how a real person behaves — not how they respond to verbal instructions.

## Slide 9
Accuracy & Calibration
The system adapts to every body — not one average
Calibration Process
▸ Subject stands in T-Pose (arms extended, legs together)
▸ 10-second hold — system automatically captures measurement
▸ 4 segment lengths measured: Hip→Knee and Knee→Foot for both legs
▸ Height estimated from headset position (±5 cm, manual override available)
▸ Personal body model created — used for all measurements in this session
▸ Re-calibration available at any time without restarting the session
Accuracy Specifications
Tracker hardware precision
±1–2 mm (HTC Vive Tracker 3.0)
Tracking update rate
90 times per second
Collision check rate
30 times per second
Minimum valid measurement
Any segment < 10 cm triggers re-calibration automatically
Height estimation
HMD position × 0.92 correction (or manual entry)
Warning threshold
10 cm (configurable 0–50 cm)
Collision threshold
3 cm (configurable 0–20 cm)
We are not testing a 'standard person.' We are testing this person, in this body, in this vehicle.

## Slide 10
The Data We Collect
Every session produces actionable engineering data
Session Summary Report (1 row per session)
▸ Subject ID & Height
▸ Individual body segment measurements (hip→knee, knee→foot)
▸ Minimum clearance recorded — per vehicle component
▸ Total warning events and collision events
▸ Which body part triggered each event + timestamp
▸ Session date, duration, and test configuration
Full Frame Data Log (optional, 10 Hz)
▸ Position of all 5 body points — recorded every 100 ms
▸ Distance to every reference point — every frame
▸ Complete 3D motion path for post-session reconstruction
▸ Full timeline of warning state changes
▸ Enables statistical analysis across multiple subjects
Output format: CSV — opens directly in Excel · compatible with statistical analysis tools · no special software needed

## Slide 11
A Typical Test Session
Driver entry/exit sequence — step by step
Approach
Subject A (178 cm, male) approaches the driver door and reaches for the handle. All clearances: SAFE No warnings triggered.
▶
Entry — Step In
Left knee swings toward dashboard during step-in motion. ⚠ WARNING Left Knee / Dashboard Clearance: 7.3 cm
▶
Seated
Subject settles into the seat position. All clearances return to SAFE. No active warnings.
▶
Exit — Step Out
Right knee catches center console during exit motion. 🔴 COLLISION Right Knee / Center Console Clearance: 1.1 cm
Post-Test Output: Minimum clearance: 1.1 cm (Right Knee / Center Console) → Engineering recommendation: Widen center console cutout by 15 mm

## Slide 12
Why This Beats Traditional Methods
Faster insights · Earlier in the process · Lower cost
Traditional Physical Testing
Our VR System
When in the process
✗ Post-prototype (too late)
✓ Pre-prototype (early design)
Cost per test
✗ High — prototype + lab time
✓ Low — virtual, fully repeatable
Time to set up
✗ Days to weeks
✓ Minutes
Data output
✗ Subjective verbal feedback
✓ Quantified distance & collision data
Design iteration
✗ New physical prototype required
✓ Change digital model, retest same day
Subject variation
✗ Difficult to control
✓ Same protocol every time, any body
Collision detection
✗ Visual inspection only
✓ Millimeter-accurate, automated

## Slide 13
How It's Built
Six modular systems working together — each independently configurable
Hardware Layer
HMD headset + 5 Vive Trackers (waist, knees, feet)
▼
Body Model
Digital skeleton mirrors every movement in real time (90 FPS)
▼
Vehicle Reference
Marked target zones placed on dashboard, console, footwell, etc.
▼
Collision Detector
Measures distance from each body point to each vehicle zone (30 Hz)
▼
Feedback System
Visual darkening · Audio alert · 3D impact effect
▼
Data Logger
Saves every measurement to CSV for post-session engineering review
All six components are modular — each can be updated, swapped, or tuned independently.

## Slide 14
Business Value
Cost reduction · Speed to market · Data-driven decisions
Cost Reduction
Catching an ergonomic issue in VR — before a physical prototype exists — eliminates costly late-stage design changes. Industry estimates: 10–100× cheaper to fix in digital vs. physical prototype stage. One avoided prototype revision can fund the entire VR system.
Speed to Market
Testing does not wait for a physical vehicle to be built. Design teams can run ergonomic validation in parallel with CAD/CAM work, compressing the development timeline. Multiple design variants can be tested in a single day.
Data-Driven Decisions
Instead of: "It felt a bit tight" Engineering teams receive: "Right Knee / Center Console: min. clearance 1.1 cm at t=3.2s during door entry sequence" Every design decision is backed by measurement.

## Slide 15
Current Status & Next Steps
Core system complete — first live test session ready
Complete ✓
✓ Body tracking — 5 points, 90 FPS real-time
✓ Dynamic body model (limb segments + joint spheres)
✓ Per-subject calibration (T-Pose, 10 sec)
✓ Collision detection & distance measurement
✓ Three-level warning system (Safe / Warning / Collision)
✓ Immersive feedback (vignette, audio, impact FX)
✓ Session data logging (summary + full frame CSV)
✓ Session state management (Idle → Calibrate → Test → Review)
✓ Desktop simulation mode (no headset required for QA/review)
In Progress / Next Steps
[In Progress]
On-screen HUD (live distance display)
[In Progress]
Subject info input form
[In Progress]
Visual materials for body model
[Next]
First complete test level with vehicle mesh
[Next]
First closed-loop session with real vehicle model and human subject
[Next]
Statistical analysis across subject pool
[Future]
Multi-vehicle comparative study

## Slide 16
Designed for Humans. Validated by Data.
This solves a real human problem — ergonomic failures affect real drivers, not just metrics.
The system is measurement-first — every interaction becomes a data point, not an opinion.
It is designed to scale — any vehicle model, any body size, any team can run a session.
Questions?